## Slide 1: Compilers for Embedded Systems
Summer Term 2022
Heiko Falk
Institute of Embedded Systems
Electrical Engineering, Computer Science and Mathematics
Hamburg University of Technology

## Slide 2: Chapter 1 Introduction & Motivation

## Slide 3: Embedded Systems
Definition: Embedded Systems (ES) are
  information-processing systems
  that are embedded into a larger, surrounding product.
The fact that embedded systems process information is not decisive for a purchase
Instead: Benefit of surrounding product influences purchase decision
[P. Marwedel. Embedded System Design. Springer, 2011]

## Slide 4: Application Areas of Embedded Systems
Consumer products
Multimedia
Transportation
Telecommunication
Building management, robotics, …

## Slide 5: Relevance of Embedded Systems
Smartphones 113 m. devices 2007 ↝ 25.6% increase p.a. 365 m. devices 2012
UMTS 402 m. customers worldwide 2008 30 m. new customers per quarter
Energy consumption of mobile broadband infrastructure 42.8 m. kWh 2005 ↝ 124.4 m. kWh 2011
Broadband internet 576 m. customers 2011 ↝ 100% increase compared to
2007
US consumer electronics  household: 25 devices,  adult: 1,200$ p.a.
[www.itfacts.biz]

## Slide 6: Demands on Embedded Systems (1)
Efficiency
Runtime efficiency
Energy consumption
Code size
Physical size / weight
Cost

## Slide 7: Demands on Embedded Systems (2)
Real-Time Capabilities
Definition: For some input x, a computer system computes some f(x).
  A Non-Real-Time System is correct if it computes f(x) correctly.
  A Real-Time System is correct if the computation of f(x) completes within given time bounds.
A too late computation of f(x) by a Real-Time System is as severe as a functionally incorrect computation.

## Slide 8: Demands on Embedded Systems (3)
Real-Time Capabilities
“Hard” Real-Time System: Late computation of f(x) ↝ Catastrophic consequences (loss of human life, environmental damages, …) Example airbag control: Command to ignite the airbags: 15ms Deadline miss: Danger of injuries for passengers or saviors. Thus: Do not fire airbags
“Soft” Real-Time System: No catastrophic consequences Example DVD player: Deadline miss during frame decoding: Frame-Drop Not nice but (usually) not disastrous

## Slide 9: Demands on Embedded Systems (4)
Dependability / Safeness
Life span of embedded systems: Typically several years
During the entire lifetime: No outage
Example throttle valve control: Production volume: 2 m. units per year Allowed error rate: 1 unit per year
Maintainability, (Limited Extensibility)
Error search and diagnosis, reconfiguration during runtime
Design Automation (↝ Time to Market)
Specification, synthesis, code generation

## Slide 10: Design Process of Embedded Systems
Validation; Evaluation (Efficiency, Real-Time aspects, Energy, ...)
HW/SW Co-Synthesis
Standard-SW
(RTOS, ...)
HW com-
ponents
Implementation
Application Know-How
Specifi-
cation
HW & SW
Specifi-
cation
HW De-
sign
Binary
Code
HW/SW Co-Design
– Task scheduling
Design space exploration
HW/SW Partitioning
...
– HW Synthesis
– SW Code generation

## Slide 11: Topics of the Course
Overview
Introduction & Motivation
Compilers for Embedded Systems – Requirements & Dependencies
Internal Structure of Compilers
Pre-Pass Optimizations
HIR Optimizations and Transformations
Code Generation
LIR Optimizations and Transformations
Register Allocation
WCET-Aware Compilation
Outlook

## Slide 12: General References
Embedded Systems
Peter Marwedel. Embedded System Design. Springer, 2011. ISBN 978-94-007-0256-1 Full-text available as e-book via TUHH library: https://katalog.tub.tuhh.de/Record/1650607989
Compiler Construction
Steven S. Muchnick. Advanced Compiler Design & Implementation. Morgan Kaufmann, 1997. ISBN 978-1-55860-320-2
Andrew W. Appel. Modern compiler implementation in C. Cambridge University Press, 2004. ISBN 0-521-60765-5