## Slide 1: Compilers for Embedded Systems
Summer Term 2022
Heiko Falk
Institute of Embedded Systems
Electrical Engineering, Computer Science and Mathematics
Hamburg University of Technology

## Slide 2: Chapter 2 Compilers for Embedded Systems – Requirements & Dependencies

## Slide 3: Outline
Introduction & Motivation
Compilers for Embedded Systems – Requirements & Dependencies
Internal Structure of Compilers
Pre-Pass Optimizations
HIR Optimizations and Transformations
Code Generation
LIR Optimizations and Transformations
Register Allocation
WCET-Aware Compilation
Outlook

## Slide 4: Chapter Contents
Compilers for Embedded Systems – Requirements & Dependencies
  Code Generation Tools
    Compiler, Assembler, Linker
    Source Code, Assembly Code, Object Code, Binary Code
  Source Languages for Compilers for Embedded Systems
    C, C++, Java
  Embedded Processors
    Digital Signal Processors
    Multimedia Processors
    Very Long Instruction Word Machines
    Network Processors
  Requirements on Compilers for Embedded Systems
    Code Quality vs. Compilation Times

## Slide 5: Design Process of Embedded Systems
Validation; Evaluation (Efficiency, Real-Time aspects, Energy, ...)
Implementation
Application Know-How
Specifi-
cation
HW & SW
Specifi-
cation
HW De-
sign
Binary
Code
Standard-SW
(RTOS, ...)
HW com-
ponents
HW/SW Co-Design
– Task scheduling
Design space exploration
HW/SW Partitioning
...
– HW Synthesis
– SW Code generation
HW/SW Co-Synthesis

## Slide 6: Code Generation Tools
Assembly
Code
Object
Code
Binary
Code
Source
Code
Linker
Assembler
Compiler

## Slide 7
Source Code
Programming language, legible and comprehensible for humans
Standard constructs: Loops, procedures, variables, ...
High abstraction level: Machine-independent algorithms
Assembly Code
Symbolic machine code
Limited legibility and comprehensibility for humans
Machine language constructs: ALU operations, registers, …
Low abstraction level: Machine-specific representation
Assembly
Code
Source
Code
Compiler

## Slide 8
  Readable plain text
  No / few real addresses
  Instead: Symbolic addresses e.g., encode, h, tqmf
Assembly
Code
.align 1
.global encode
.type encode,@function
encode:
mov %d15, %d5
mov %d12, %d4
movh.a %a12, HI:h
lea %a12, [%a12] LO:h
movh.a %a13, HI:tqmf
lea %a13, [%a13] LO:tqmf
ld.w %d14, [%a13] 4
ld.w %d10, [%a12] 4
mul %d14, %d10
# Load address of array h to A12
# Load address of array tqmf to A13
# Load tqmf[1] to D14
# Load h[1] to D10
# Multiply

## Slide 9
Object Code
Binary representation of assembly code, no longer legible
No plain text mnemonics, 0/1 bit sequences instead
Whenever possible, symbolic addresses replaced by real ones
Assembler
Line-by-line translation Assembly instructions  machine instructions
Within a single assembly file: Address Resolution
Object
Code
Assembly
Code
Assembler

## Slide 10
Translation (Example: Infineon TriCore 1.3)
Address Resolution
Symbolic address h declared in very same assembly file:
  Symbol h is known to assembler
  Replacement of h by relative address, relative within the object file
h is unknown to assembler:
  Defer address resolution at a later point in time
Object
Code
MUL D[a], D[b] (SRR)
b
a
0xE2
15
12
11
8
7
0
mul %d14, %d10
1010 1110 11100010

## Slide 11
Binary Code
Executable program representation
All symbolic addresses replaced by real addresses
Lowest possible abstraction level
Linker
Union of many object files and libraries to a single, executable program
Address resolution using libraries of object code
Layout of code in memory
Binary
Code
Object
Code
Linker

## Slide 12
Example Address Resolution
Object code contains jump to external function: call abs
Search abs in all other object files and libraries
Add code of abs to binary executable file
Example Memory Layout of Binary Code
Binary code consists of functions decode, encode, abs, main
Memory layout finally defines effective addresses
Binary
Code
decode
encode
abs
main
decode
encode
abs
main

## Slide 13: Chapter Contents
Compilers for Embedded Systems – Requirements & Dependencies
  Code Generation Tools
    Compiler, Assembler, Linker
    Source Code, Assembly Code, Object Code, Binary Code
  Source Languages for Compilers for Embedded Systems
    C, C++, Java
  Embedded Processors
    Digital Signal Processors
    Multimedia Processors
    Very Long Instruction Word Machines
    Network Processors
  Requirements on Compilers for Embedded Systems
    Code Quality vs. Compilation Times

## Slide 14: Source Languages for Compilers for Embedded Systems
In the following
Brief digest of most common programming languages
No claim to be complete!
Imperative Programming Languages
C
Object-Oriented Programming Languages
C++
Java

## Slide 15: ANSI-C: Properties (1)
Purely Imperative
  No object-orientation: No classes, no objects
  C-Program: Set of functions
  Function main: Standardized starting point
  Functions: Sequence of statements, execution in sequential order
int filtep( int rlt1, int al1, int rlt2, int al2 )
{
long pl, pl2;
pl = 2 * rlt1;
pl = (long) al1 * pl;
pl2 = 2 * rlt2;
pl += (long) al2 * pl2;
return( (int)(pl >> 15) );
}

## Slide 16: ANSI-C: Properties (2)
Standardized Programming Language
  ISO/IEC 9899:1999 (E)
Standard Data Types
  signed / unsigned char
  signed / unsigned short
  signed / unsigned int
  signed / unsigned long
  signed / unsigned long long
  float, double, long double, _Bool

## Slide 17: ANSI-C: Properties (3)
Composed Data Types
  Arrays
  Structures
  Variants
int h[ 3 ];
h[ 1 ] = 42;
h
0
1
2
struct point { int x; char y; } p;
p.x = 42;
p
x
y
union point { int x; char y; } p;
p.y = 42;
p
x / y
42
42
42

## Slide 18: ANSI-C: Properties (4)
Pointers and Memory Management
  Pointers
int h[ 3 ];
int *p = &h[ 1 ];
h[ 1 ] = 42;
*p = 12;
h
0
1
2
42
p

## Slide 19: ANSI-C: Properties (5)
Pointers and Memory Management
  Pointers
  Dynamic memory management
int h[ 3 ];
int *p = &h[ 1 ];
h[ 1 ] = 42;
*p = 12;
h
0
1
2
12
p
char *p = (char *) malloc( 100 );
p[ 1 ] = 42;
free( p );
/* Allocation of 100 Bytes */
/* Memory deallocation */
Dynamic memory management explicitly by programmer!

## Slide 20: ANSI-C: Properties (6)
Architecture-Dependence & Unspecified Behavior
  Bit-width of int  word-length of a CPU int on 16-bit machine: [ -32768, 32767 ] int on 32-bit machine: [ -2147483648, 2147483647 ]
  Behavior of >> operator (shift right) logic shift – Most Significant Bit (MSB) filled with ‘0’: arithmetic shift – MSB filled with old MSB:
  Signedness of char: signed char [ -128, 127 ] vs. unsigned char [ 0, 255 ]
-8 >>l 1 = 1000 >>l 1 = 0100 = 4
-8 >>a 1 = 1000 >>a 1 = 1100 = -4

## Slide 21: ANSI-C: Discussion
Pros
Standardized, widespread programming language
Many (freely available) existing code generation tools
Large already existing source code base (open source & proprietary)
Despite high abstraction level: Low-level programming still possible
Machine-orientation
Effort to construct a compiler still acceptable
Cons
Machine-orientation, lacking portability of source code
Programmer-responsible memory management error-prone
No object-orientation

## Slide 22: ANSI-C++: Properties
ANSI-C + Object-Orientation + …
Classes & Objects
Elements, member functions/methods
Constructors & destructors
Inheritance
Protection of class elements: public, protected, private
Virtual methods & polymorphic classes
Exception handling
Generic programming: Templates
Standard Template Library (STL)

## Slide 23: ANSI-C++: Pros
Higher-order programming language, fulfills desire for OO in Embedded Systems
Existing ANSI-C source codes can often be adopted
Wide dissemination
Many (freely available) existing code generation tools
Large already existing source code base (open source & proprietary)
Despite high abstraction level: Low-level programming still possible
Machine-orientation

## Slide 24: ANSI-C++: Cons (1)
Some C++ constructs lead to high overheads, too high for Embedded Systems
  Time between throwing and catching unclear due to destructors
  Increased memory consumption due to internal data structures
Example Exceptions:
try {
object o;
...
Code…;
}
catch( E ) {
// Error handling
}
Exception E is thrown here...
... and caught here
o must
be
destroyed!

## Slide 25: ANSI-C++: Cons (2)
  B and C both feature a very own implementation of bar().
  High run-times due to dynamic type checking and method lookup.
Example Purely Virtual Classes:
class A {
virtual bar() = 0;
}
class B : public A { class C : public A {
virtual bar(); virtual bar();
} }
A *foo; ...; foo->bar(); // B::bar()?? C::bar???

## Slide 26: Embedded C++
Subset of C++, Specifically Designed for Embedded Systems
No purely virtual classes
No exceptions
No templates
No namespaces (“Features such as namespaces […] are difficult to understand, increasing the chances of programmer errors.”)
No multiple inheritance
No STL data structures (Standard Template Library)
[Embedded C++ Slashes Code Size And Boosts Execution.
www.ghs.com/wp/ec++article2.html]

## Slide 27: Java: Pros
Programming Language with consequent object-oriented design
Modular structure, allows for excellent SW abstraction
Good type mechanisms
Good language constructs for modelling of behavior and control
Mathematical model similar to C++, but said to be better
Transparent memory protection, automatic Garbage Collection
Code said to be better legible than C++
No pointers
Java Byte Code Interpreter: High portability of Java source code

## Slide 28: Java: Cons
Enormous Resource Demands
Disadvantages of Java’s OO constructs similar to C++
Byte code interpretation during run-time
Just-In-Time translation often infeasible for Embedded Systems
Real-time behavior of Garbage Collection?
Today: Even lean Java (EmbeddedJava) unsuitable for systems that have to be fast and are resource-constrained
Excerpt from Sun’s (ancient) license agreement for Java:
”Software is not designed or licensed for use in on-line control of aircraft, air traffic, aircraft navigation or aircraft communications; or in the design, construction, operation or maintenance of any nuclear facility.”
[Formerly at java.sun.com/products/plugin/1.2/license.txt]

## Slide 29: Chapter Contents
Compilers for Embedded Systems – Requirements & Dependencies
  Code Generation Tools
    Compiler, Assembler, Linker
    Source Code, Assembly Code, Object Code, Binary Code
  Source Languages for Compilers for Embedded Systems
    C, C++, Java
  Embedded Processors
    Digital Signal Processors
    Multimedia Processors
    Very Long Instruction Word Machines
    Network Processors
  Requirements on Compilers for Embedded Systems
    Code Quality vs. Compilation Times

## Slide 30: Digital Signal Processors
Properties
Optimized for digital signal processing (e.g., filters, Fourier transformation, ...)
Heterogeneous register files, grouped for special purposes
Limited parallelism during instruction execution
Dedicated address generation units / addressing modes
Multiply-Accumulate instruction (a = a + b * c)
Zero-Overhead Loops
Saturating arithmetic
Efficiency and real-time capabilities extremely important

## Slide 31: DSPs: Heterogeneous Register Files (1)
Example Infineon TriCore 1.3:
Separate address & data registers
A15
A14
A13
A12
A11
A10
A9
A8
A7
A6
A5
A4
A3
A2
A1
A0
Address Registers
Data Registers
D15
D14
D13
D12
D11
D10
D9
D8
D7
D6
D5
D4
D3
D2
D1
D0

## Slide 32: DSPs: Heterogeneous Register Files (2)
Example Infineon TriCore 1.3:
Separate address & data registers
Registers with particular meaning
64-bit data registers (extended Registers)
Upper & lower context (UC & LC): UC automatically saved during function call, LC not
A15 (Implicit AREG)
A14
A13
A12
A11 (Return Addr)
A10 (Stack Ptr)
A9 (Global AREG)
A8 (Global AREG)
A7
A6
A5
A4
A3
A2
A1 (Global AREG)
A0 (Global AREG)
Address Registers
Data Registers
D15 (Implicit DREG)
D14
D13
D12
D11
D10
D9
D8
D7
D6
D5
D4
D3
D2
D1
D0
E14
E12
UC
E8
E6
E4
E2
E0
LC
E10
[Infineon AG. TriCore User’s Manual, Volume 1. 2008]

## Slide 33: DSPs: Limited Parallelism
Example Infineon TriCore 1.3:
Integer Pipeline: Arithmetical/logical instructions, conditional branches
Load/Store Pipeline: Memory accesses, address computations, unconditional branches, function calls
Loop Pipeline: Loop instructions
Limited Parallelism:
  Pipelines work independently / parallel in the ideal case
  If not the ideal case: Stall in L/S Pipeline  Stall in I-Pipeline and vice versa

## Slide 34: DSPs: Address Generation Units (AGUs)
General Structure of Address Generation Units:
Address
register
Effective
address
AR
pointer
Immediate
value
Address registers (AR) contain effective addresses for memory accesses
Instruction word encodes which AR to use (AR pointer)
ARs can be loaded with constants explicitly encoded in the machine instruction (immediate operands)

## Slide 35: DSPs: Address Generation Units (AGUs)
General Structure of Address Generation Units:
ARs can be in-/decreased via a simple ALU
Increment / decrement by offset given as immediate operand
Increment / decrement by constant “1” as offset
+ -
”1”
Address
register
Effective
address
AR
pointer
Immediate
value
Offset

## Slide 36: DSPs: Address Generation Units (AGUs)
General Structure of Address Generation Units:
Increment / decrement by contents of Modifier Register (MR)
Instruction word encodes which MR to use (MR pointer)
MRs can be loaded explicitly with immediate values
+ -
”1”
Modifier
register
Address
register
Effective
address
AR
pointer
MR
pointer
Immediate
value
Offset

## Slide 37: DSPs: Address Generation Units (AGUs)
General Structure of Address Generation Units:
Load AR: AR = <const>
Load MR: MR = <const>
Modify AR: AR  <const>
Auto-Increment: AR  “1”
Auto-Modify: AR  MR
“Auto”-operations: Parallel to data path, no extra run-time, highly efficient!
All others: Need extra instruction for data path, less efficient.
+ -
”1”
Modifier
register
Address
register
Effective
address
AR
pointer
MR
pointer
Immediate
value
Offset

## Slide 38: DSPs: Conventional Loop Code
C-Code of a Loop: Conventional Assembly Code:
(TriCore 1.3)
Properties
Decrement & conditional branch: Both in Integer Pipeline  no parallel execution of these instructions
2 clock cycles * 10 iterations = 20 cycles (min.) loop overhead
In presence of delay slots for branches even worse!
int i = 10;
do {
...
i--;
} while ( i );
mov %d8, 10;
.L0:
...
add %d8, -1;
jnz %d8, .L0;

## Slide 39: DSPs: Optimized Loop Code
C-Code of a Loop: Zero-Overhead Loops:
(TriCore 1.3)
Properties
Decrement & conditional branch: Parallel in Loop Pipeline
loop instruction: Consumes run-time only in 1st and last iteration  only 2 clock cycles loop overhead
int i = 10;
do {
...
i--;
} while ( i );
mov %a12, 10;
.L0:
...
loop %a12, .L0;

## Slide 40: Problem of Standard Wrap-Around Computer Arithmetic (1)
Standard Arithmetic leads to Wrap-Around in case of Over-/Underflows
Problem: Computed results with Wrap-Around are…
  not only incorrect
  but also implausible / not even close to the correct solution
The resulting error is maximal (most-significant bit position 2n gets lost), not minimal! Example: (4 bits, 2’s compl.): |(7 +wrap 1) –exact (7 +exact 1)| = |(0111(2) +wrap 0001(2)) –exact 8)| = |1000(2) –exact 8| = |-8 –exact 8| = 16

## Slide 41: Problem of Standard Wrap-Around Computer Arithmetic (2)
Large deviation between computed result (with overflow) and desired result, highly dramatic during signal processing (e.g., amplifying of an audio signal / luminance adjustment of an image pixel)

## Slide 42: Lesser Error with Saturating Arithmetic
Saturating arithmetic for additions or multiplications yields the maximally/minimally representable value in case of over-/underflows.
Examples
Absolute value representation (4 bits, unsigned): 8 +sat 8 = 1000(2) +sat 1000(2) = 7 +sat 11 → 15 ≠ 18 10000(2) → 1111(2) = 15 ≠ 16
2’s complement representation (4 bits, signed): 7 +sat 1 = 0111(2) +sat 0001(2) = -5 –sat 7 → -8 ≠ -12 1000(2) → 0111(2) = 7 ≠ 8
In particular, saturating arithmetic never produces sign inversions!

## Slide 43: Another Example
a 0111 b + 1001 Standard Wrap-Around arithmetic (1)0000 Saturating arithmetic 1111 (a+b)/2: correct 1000 Wrap-Around arithmetic 0000 Saturating arithmetic using >> 0111 „almost correct“
Suitable for DSP / multimedia applications
  Interrupts generated by overflows  Real-time requirements violated…?
  Exact values of less importance anyway
  Wrap-Around arithmetic produces inferior results

## Slide 44: Saturating Arithmetic: Discussion
Pros
More plausible results in case of over-/underflows
Cons
More time-consuming to compute
Associativity and other laws violated
DSPs usually allow to choose between saturating and standard arithmetic (they feature correspondent variants of machine instructions)
“Saturation” in IEEE 754 floating point standard:
Over-/underflows produce ± infinity as result
Further IEEE 754 operations do not change this result!

## Slide 45: DSPs: Real-Time Capabilities
The Timing Behavior of a Processor should be predictable!
Properties causing trouble:
Accesses to shared hardware resources
  Caches with replacement strategies with problematic timing behavior
  Unified caches for both code and data (conflicts between data and instructions)
  Pipelines with stall cycles (“bubbles”)
  Multi-cores with unpredictable communication/bus delays
Branch prediction, speculative instruction execution
Interrupts that can happen at any time
Memory refreshes at any time
Machine instructions with data-dependent execution latencies
Avoid as many of these problematic properties as possible

## Slide 46: Multimedia Processors
Properties
Optimized for, e.g., image and audio processing
Well-known commercial products: Intel MMX, SSE or SSE2; AMD 3DNow!; Sun VIS; PowerPC AltiVec; HP MAX
Motivation: Multimedia software often does not use the full word-length of a processor (i.e., int), but only parts of it (e.g., short or char).
SIMD principle: Single Instruction, Multiple Data
Parallel handling of several “little” pieces of data by 1 machine instruction

## Slide 47: SISD vs. SIMD Execution
Exercise: Perform two Additions of 2 short Variables each
SISD principle (Single Instruction, Single Data): Load first 2 summands in registers, int addition, Load second 2 summands in registers, int addition
Costs: 2 full additions
SIMD principle (Single Instruction, Multiple Data): Load first 2 summands in upper halves of registers, Load second 2 summands in lower halves of registers, SIMD addition
Costs: 1 addition

## Slide 48: Illustration SIMD Addition
SIMD Half-Word Addition:
SIMD instructions also common for quarter-words: 4 parallel char additions for a 32-bit processor

## Slide 49: Very Long Instruction Word (VLIW)
Motivation Performance boost by exploiting instruction-level parallelism
Conventional Processors:
1 integer ALU
1 multiplier
1 (heterogeneous) register file
VLIW Processors:
n integer ALUs
n multipliers
n (heterogeneous) register files
Interconnection network

## Slide 50: Example: M3 VLIW Processor
MAC
ALU
REG
  Slice 0
MAC
ALU
REG
  Slice 1
MAC
ALU
REG
  Slice 15
Interconnection Network
Group Memory

## Slide 51: VLIW Instruction Word
1 instruction word contains 1 VLIW machine instruction
1 VLIW instruction contains n VLIW operations
Each operation controls exactly one Functional Unit (FU)
Fixed matching of operations in the instruction with FUs: Operation 0  FU 0, Operation 1  FU 1, ...
  Slice 0
  Slice 1
  Slice 15
Interconnection Network
Group Memory
  Op0
  Op1
  Op15
VLIW instruction

## Slide 52: Network Protocols
Communication between distant Processors
Communication media error-prone
Payload is divided into packets
Packets are augmented with additional information (Header)
Example IPv4 Header:
Version
Length
Service Code
Total Packet Length
Identification
Flags
Fragment Offset
Time To Live
Protocol
Header Checksum
Source IP Address
Destination IP Address
0
7
15
23
26
31

## Slide 53: Bit Packets (1)
Bit Packets in Protocol Headers
Headers are divided in regions with different meaning
These bit regions are not aligned with processor word-lengths
Bit packet:
  Sequence of consecutive bits
  of arbitrary length
  starting at arbitrary bit positions
  and eventually crossing word boundaries
Efficient manipulation of data at bit-level necessary!

## Slide 54: Bit Packets (2)
Network Processing Units (NPUs)
Software for network protocol processing: High amount of code dealing with processing of bit packets
Typical C-Code (GSM kernel, TU Berlin):
Instruction set of NPUs: Special-purpose machine instructions to extract, insert & manipulate bit packets
xmc[0] = (*c >> 4) & 0x7;
xmc[1] = (*c >> 1) & 0x7;
xmc[2] = (*c++ & 0x1) << 2;
xmc[2] |= (*c >> 6) & 0x3;
xmc[3] = (*c >> 3) & 0x7;

## Slide 55: Operations on Bit Packets
Extraction of Bit Packets
Insertion of Bit Packets
extr R2, R0, <Offset1>, <size>;
Register R0
Register R1
Register R2
Offset1
Size
insert R0, R2, <Offset2>, <size>;
Register R0
Register R1
Offset2
Size
Register R2

## Slide 56: Chapter Contents
Compilers for Embedded Systems – Requirements & Dependencies
  Code Generation Tools
    Compiler, Assembler, Linker
    Source Code, Assembly Code, Object Code, Binary Code
  Source Languages for Compilers for Embedded Systems
    C, C++, Java
  Embedded Processors
    Digital Signal Processors
    Multimedia Processors
    Very Long Instruction Word Machines
    Network Processors
  Requirements on Compilers for Embedded Systems
    Code Quality vs. Compilation Times

## Slide 57: Most Important Requirements on Compilers for ES
Maximal Code Quality
Run-time efficiency
Low energy consumption
Low code size
Meaningful Measures
Best-possible mapping of source language to machine language
Exploitation of strong compiler optimizations
Reuse of code fragments
Maximal exploitation of fast and small memories
Consideration of the WCET (Worst-Case Execution Time)
...
Maximal parallelization
Real-time ability
...

## Slide 58: Less Important Requirements
Speed of the Compiler Itself
Situation for “standard” desktop computers:
  Large amount of available resources
  Code quality of less interest
  Compilers shall quickly generate correct code
Situation for Embedded Systems:
  Code quality of utmost importance
  Compiler shall generate highly-optimized code
  In the design process of Embedded Systems, compilers are called less frequently than when programming for desktop computers
 High Run-Times of Optimizing Compilers are acceptable!

## Slide 59: References
Code Generation Tools
John R. Levine. Linkers & Loaders. Morgan Kaufmann, 2000. ISBN 1-55860-496-0
Programming Languages
Brian W. Kernighan, Dennis M. Ritchie. The C Programming Language. Prentice Hall, 1988. ISBN 0-13-110362-8
Embedded C++ Home Page. http://www.caravan.net/ec2plus, 2002.
The Real-Time Specification for Java. http://www.rtsj.org, 2007.

## Slide 60: References
Processors & Instruction Sets
Peter Marwedel. Embedded System Design. Springer, 2011. ISBN 978-94-007-0256-1
Rainer Leupers. Code Optimization Techniques for Embedded Processors. Kluwer Academic Publishers, 2000. ISBN 0-7923-7989-6
Jens Wagner. Retargierbare Ausnutzung von Spezialoperationen für Eingebettete Systeme mit Hilfe bitgenauer Wertflussanalyse. Dissertation University of Dortmund, Computer Science 12, 2006.

## Slide 61: Summary (1)
Code Generation Tools
Assembler and linker as further important tools besides compilers
Address resolution, memory layout and libraries
Source Languages for Compilers for Embedded Systems
ANSI-C: widespread imperative programming language; allows machine-oriented low-level programming; error-prone memory management; unspecified language details
C++: similar to C; high overhead due to some object-oriented language constructs
Java: very high overhead due to byte code interpretation; no real-time capabilities due to dynamic garbage collection during run-time
ANSI-C most common programming language for Embedded Systems

## Slide 62: Summary (2)
Embedded Processors
Partially highly specialized instruction sets (multiply-accumulate, insert/extract, SIMD)
Special registers and address generation units
High degree of parallelism (several pipelines, multitude of functional units)
Requirements on Compilers for Embedded Systems
Code quality primary concern
Compile-times only secondary, in contrast to compilers for desktop computers