## Slide 1: Compilers for Embedded Systems
Summer Term 2022
Heiko Falk
Institute of Embedded Systems
Electrical Engineering, Computer Science and Mathematics
Hamburg University of Technology

## Slide 2: Chapter 5 HIR Optimizations and Transformations

## Slide 3: Outline
Introduction & Motivation
Compilers for Embedded Systems – Requirements & Dependencies
Internal Structure of Compilers
Pre-Pass Optimizations
HIR Optimizations and Transformations
Code Generation
LIR Optimizations and Transformations
Register Allocation
WCET-Aware Compilation
Outlook

## Slide 4: Chapter Contents
HIR Optimizations and Transformations
  Motivation
  Function Specialization / Procedure Cloning
    General-Purpose Functions in specialized Contexts
    Interlude: Standard Optimizations & WCET Estimation
    Function Specialization and WCETs
    Results (WCETEST, ACET, Code Size)
  Parallelization for Homogeneous Multi-DSPs
    Introduction, Multi-DSP Architectures
    Program Recovery
    Data Partitioning & Strip Mining
    Parallelization
    Memory Assignment, Array Descriptors, DMA
    Results

## Slide 5: Motivation of HIR Optimizations
High-Level IRs:
Very close to source language
High-level language constructs (esp. loops, function calls with parameter passing, array accesses) preserved
High-Level Optimizations
Exploit particularly these HIR features
Focus on strong reorganization of loops and function relationships
Are difficult to realize at lower abstraction levels, since required high-level information (e.g., loop bounds or function call relationships) get lost and are difficult to reconstruct

## Slide 6: Chapter Contents
HIR Optimizations and Transformations
  Motivation
  Function Specialization / Procedure Cloning
    General-Purpose Functions in specialized Contexts
    Interlude: Standard Optimizations & WCET Estimation
    Function Specialization and WCETs
    Results (WCETEST, ACET, Code Size)
  Parallelization for Homogeneous Multi-DSPs
    Introduction, Multi-DSP Architectures
    Program Recovery
    Data Partitioning & Strip Mining
    Parallelization
    Memory Assignment, Array Descriptors, DMA
    Results

## Slide 7: Function Specialization
Also Called “Procedure Cloning”
Rather old and well-known compiler technique (1993)
Goals: To enable other optimizations, to reduce the overhead to pass parameters during function calls
Approach: Of particular functions, specialized copies (“clones”) are created which have less parameters than the original function
Specialization so-called Interprocedural Optimization
Explicit consideration of calling relationships between functions during an optimization
In Contrast to Intraprocedural Optimizations
Optimization just locally inside a function f, without consideration of functions that f calls, or by which f is called

## Slide 8: Typical Function Calls
Observations
f is called several times
f has 3 arguments
Arguments n and p are instantiated several times with constants 5 and 2
int f( int *x, int n, int p ) {
for (i=0; i<n; i++) {
x[i] = p * x[i];
if ( i == 10 ) { ... }
}
return x[n-1];
}
int main() {
... f( y, 5, 2 ) ...
... f( z, 5, 2 ) ...
return f( a, 5, 2 );
}

## Slide 9: More Observations
f is so-called general-purpose function: Via parameter n, an array x of arbitrary size can be treated
Control flow in f depends on function parameter
f is used in main in a special-purpose context: Processing of arrays of size n = 5.
int f( int *x, int n, int p ) {
for (i=0; i<n; i++) {
x[i] = p * x[i];
if ( i == 10 ) { ... }
}
return x[n-1];
}
int main() {
... f( y, 5, 2 ) ...
... f( z, 5, 2 ) ...
return f( a, 5, 2 );
}

## Slide 10: Specialization of General-Purpose Functions
int f( int *x, int n, int p ) {
for (i=0; i<n; i++) {
x[i] = p * x[i];
if ( i == 10 ) { ... }
}
return x[n-1];
}
int main() {
... f_5_2( y ) ...
... f_5_2( z ) ...
return f_5_2( a );
}
int f_5_2( int *x ) {
for (i=0; i<5; i++) {
x[i] = 2 * x[i];
if ( i == 10 ) { ... }
}
return x[4];
}

## Slide 11: Expected Effects of Specialization
Reduction of the Average-Case Execution Time ACET due to
Enabling of other standard compiler optimizations inside the specialized function
Less code to be executed for parameter passing when calling the specialized function

## Slide 12: Standard Optimizations after Cloning (1)
Constant Folding
Pre-computation of expressions with purely constant operands already at compile-time
Example: Original code + Cloning + ConstFold a = p * n; a = 2 * 5; a = 10;
<INTERLUDE>

## Slide 13: Standard Optimizations after Cloning (2)
Constant Propagation
Replacement of accesses to variables that provably have constant content by the constant itself
Example: Original code + Cloning + ConstFold + ConstProp a = p * n; a = 2 * 5; a = 10; for (…; i<a; …) for (…; i<a; …) for (…; i<10; …)
<INTERLUDE>

## Slide 14: Standard Optimizations after Cloning (3)
Strength Reduction
Replacement of computationally expensive computations (e.g., multiplications, divisions, ...) by “cheaper” operations (e.g., additions, subtractions, shifts, ...)
Example: Original code + Cloning + StrengthRed x[i] = p*x[i]; x[i] = 2*x[i]; x[i] = x[i]<<1;
<INTERLUDE>

## Slide 15: Standard Optimizations after Cloning (4)
Control Flow Optimizations
Determination of possible value ranges of variables after constant folding and propagation; removal of redundant if-statements whose conditions are always true or always false ( see also chapter 4 – Loop Nest Splitting / Condition Satisfiability)
Example: Original code + Cloning + ControlFlowOpt for(i=0;i<n;i++) for(i=0;i<5;i++) for(i=0;i<5;i++) { { { …; …; …; if (i==10) …; if (i==10) …; } } }
</INTERLUDE>

## Slide 16: Expected Effects of Specialization
Reduction of the Average-Case Execution Time ACET due to
Enabling of other standard compiler optimizations inside the specialized function
Fewer code for parameter passing to be executed when calling the specialized function
Increase of Code Size due to
Generation of potentially many novel, specialized clones

## Slide 17: Impact of Cloning on WCET Estimation
Function Specialization and WCET considered only in very recent research
Recall
Worst-Case Execution Time WCET: Upper bound of a program’s run-time over all possible input data
WCET Estimation
Via static analysis of the binary code of executable programs
In the following: Workflow of the static WCET Analyzer aiT
[AbsInt Angewandte Informatik GmbH,
http://www.absint.com/ait, Saarbrücken, 2020]

## Slide 18: Workflow of the WCET Analyzer aiT (1)
Input: Binary executable P to be analyzed
exec2crl: Disassembler, translates P into aiT’s low-level intermediate representation CRL2
Value analysis: Computes possible contents of processor registers for any point in time during P’s execution. Note: P is never executed by aiT! P is „only“ analyzed.
<INTERLUDE>

## Slide 19: Workflow of the WCET Analyzer aiT (2)
Loop bound analysis: Tries to determine lower and upper bounds for the number of iterations of each loop in P.
Cache analysis: Makes use of a formal cache model, classifies each memory access in P as definite cache hit, definite cache miss, or unknown.
<INTERLUDE>

## Slide 20: Workflow of the WCET Analyzer aiT (3)
Pipeline analysis: Includes an accurate model of the processor’s pipeline. Depending on the pipeline’s initial state, possible cache states etc., possible states of the pipeline at the end of each basic block of P are determined. Result of the pipeline analysis is the WCETEST of each individual basic block.
<INTERLUDE>

## Slide 21: Workflow of the WCET Analyzer aiT (4)
Path analysis: Models all possible execution paths within P under consideration of the WCETEST of all basic blocks. Determines the longest possible execution path within P which leads to the overall WCETEST of P. Result of the path analysis is, e.g., the length of this longest path, i.e., P’s WCETEST.
<INTERLUDE>

## Slide 22: Workflow of the WCET Analyzer aiT (5)
Control Flow Graph (CFG)
Fundamental code representation during path analysis
Definition: CFG = (V, E, s) is a directed graph with
V = { b1, ..., bn } (set of all basic blocks, cf. chapter 2)
E = { (bi  bj) | basic block bj can be executed immediately after bi }
s  V = the unique start node of the CFG
<INTERLUDE>
int fun2() {
for (; a1<30; a1++ ) {
for (; b1<a1; b1++ )
printf( “%d\n”, b1 );
printf( „%d\n“, a1 );
}
return a1; }

## Slide 23: Complexity Issues
Problem: WCET analysis is not computable with today’s machines! If WCET were computable, one could decide in O(1) if WCET <  and thus solve the Halting problem.
Reason: It is not computable how long P stays in loops. Automatic loop bound analysis is applicable only to simple classes of loops. (Analogously for recursive function calls.)
<INTERLUDE>

## Slide 24: Annotations for WCET Analysis
<INTERLUDE>
</INTERLUDE>
Solution: The user of aiT must mandatorily provide information about, e.g., minimal and maximal iteration bounds of loops and recursion depths.
Annotation file: Contains such user-provided annotations (“flow facts”) and is – besides the program P to be analyzed – another external input to aiT.

## Slide 25: Why Specialization and WCETEST?
Motivation
Frequent occurrences of general-purpose functions in special-purpose contexts in embedded software
Loop bounds are particularly often controlled by function parameters
Loop bounds are particularly critical for WCET estimates
Procedure Cloning allows the extremely precise annotation of loop bounds for WCET analysis
[P. Lokuciejewski. Influence of Procedure Cloning on WCET Prediction. CODES+ISSS, Salzburg, 2007]

## Slide 26: Loop Bound Annotations & Cloning (1)
Original code
Loop annotation extremely imprecise since annotation must cover all invocations of f.
int f( int *x, int n, int p ) {
// loopbound min 0, max n
for (i=0; i<n; i++ ) {
x[i] = p * x[i];
if ( i == 10 ) { ... }
}
return x[n-1];
}
If f is called somewhere with n = 2,000 as maximal value, 2,000 loop iterations have to be considered always.
For calls like, e.g., f( a, 5, 2 ), 2,000 loop iterations are likewise assumed
Heavy WCET overestimation

## Slide 27: Loop Bound Annotations & Cloning (2)
Cloned code
Loop annotation extremely precise since annotation covers all invocations of f_5_2 exactly.
For calls like, e.g., f_5_2( a ), exactly 5 iterations are assumed
Exact WCET estimation
Original function f or other additional clones of f are fully independent of annotations in f_5_2
No interdependencies between all these versions of f w.r.t. WCET analysis
int f_5_2( int *x ) {
// loopbound min 5, max 5
for (i=0; i<5; i++ ) {
x[i] = 2 * x[i];
if ( i == 10 ) { ... }
}
return x[4];
}

## Slide 28: Realization of Function Specialization (1)
Caution when Applying Function Specialization
Increase of code size during cloning must not be neglected!
Cloning of every possible function which is called at least twice with the same constant as argument is usually unacceptable
Parameter-Driven Application of Function Specialization
Size G: Never clone a function f which is larger than G
Amount of constant arguments K: clone a function f only if at least K% of all calls of f contain constant arguments that can be used for cloning

## Slide 29: Realization of Function Specialization (2)
Given
Function f to be specialized
Dictionary arg that maps the arguments of f to be specialized to the constant values to be used
Approach Using HIR ICD-C
Create new function type T’ that corresponds to the Type T of f, but without those arguments from arg to be specialized
Create new function symbol S’ of type T’; add S’ to that symbol table in which f is declared
Create a copy f’ of the code of f with function symbol S’; add f’ to the same compilation unit that also holds f

## Slide 30: Realization of Function Specialization (3)
Given
Function f to be specialized
Dictionary arg that maps the arguments of f to be specialized to the constant values to be used
Approach Using HIR ICD-C (ctd.)
For each argument a  arg to be specialized:
  Create new local variable v’ in f’
  Create assignment v’ = <arg[a]>; at the very beginning of f’
  Replace each occurrence of a in f’ by v’

## Slide 31: Realization of Function Specialization (4)
Given
Function f to be specialized
Dictionary arg that maps the arguments of f to be specialized to the constant values to be used
Approach Using HIR ICD-C (ctd.)
For each function call c of f to be specialized:
  Remove all arguments a  arg to be specialized from the parameter list of c
  Replace called function f by f’ within c

## Slide 32: Workflow of Function Specialization
Function specialization
Constant folding & propagation
Strength reduction
If-statements
G = 2,000 ICD-C expressions
K = 50%
Considered Processors
Infineon TriCore TC1796
ARM 7 TDMI (ARM and THUMB instruction sets)

## Slide 33: Relative WCETEST after Procedure Cloning
WCETEST reductions from 13% up to 95%!
Chart: Rel. WCETEST [%]
| TriCore | ARM | Thumb
EPIC | 0.0539 | 0.0428 | 0.0435
MPEG2 | 0.7008 | 0.6675 | 0.6655
GSM | 0.8186 | 0.8727 | 0.6897
Geo. Mean | 0.31387 | 0.29214 | 0.27129
Notes: EPIC: 1 Filter-Funktion, die geklont wird, enthält 32 Schleifen, die z.T. vierfach-verschachtelt sind. Die Schleifeniterationen hängen z.T. von Funktionsargumenten ab. Diese Funktion wird oft (6x) aufgerufen, nach Cloning ist jeder dieser Aufrufe spezialisiert und mit exakten Flow Facts annotiert.
GSM: Filter-Funktion, die mit Konstanten 13, 14 und 120 aufgerufen wird, die die Schleifeniterationen steuert. Ursprünglich muss diese Schleife mit dem max-Wert 120 annotiert werden, was nach Cloning viel präziser gemacht werden kann.

## Slide 34: Relative ACETs after Procedure Cloning
Marginal ACET reductions of 3% max.
Impact of overhead for parameter passing and of successive optimization on ACET apparently negligible.
Chart: Rel. ACET [%]
| TriCore | ARM | Thumb
EPIC | 1.0002 | 0.9819 | 0.9703
MPEG2 | 0.9979 | 0.9873 | 0.9735
GSM | 0.9999 | 1 | 1.0006
Geo. Mean | 0.99933 | 0.9897 | 0.98137

## Slide 35: Relationship between WCETEST and ACET
Very Astonishing
How can one and the same optimization have such a different influence on seemingly similar criteria like WCETEST and ACET?
Reasons
Code before cloning only poorly annotatable  aiT computes quite imprecise WCET estimates
Code after cloning precisely annotatable  aiT computes much more precise WCET estimates
Specialization obviously improves tightness of WCETEST considerably ( cf. chapter 3 – Objective Functions)
The real (and unknown) WCETs are expected to be reduced only as marginally as ACETs are

## Slide 36: Relative Code Sizes after Procedure Cloning
Code size increases from 2% up to 225%!
Chart: Rel. Code Size [%]
| TriCore | ARM | Thumb
EPIC | 3.2657 | 3.0505 | 3.2975
MPEG2 | 1.2894 | 1.2336 | 1.22
GSM | 1.019 | 1.0328 | 1.0314
Geo. Mean | 1.625 | 1.5722 | 1.6069

## Slide 37: Chapter Contents
HIR Optimizations and Transformations
  Motivation
  Function Specialization / Procedure Cloning
    General-Purpose Functions in specialized Contexts
    Interlude: Standard Optimizations & WCET Estimation
    Function Specialization and WCETs
    Results (WCETEST, ACET, Code Size)
  Parallelization for Homogeneous Multi-DSPs
    Introduction, Multi-DSP Architectures
    Program Recovery
    Data Partitioning & Strip Mining
    Parallelization
    Memory Assignment, Array Descriptors, DMA
    Results

## Slide 38: Parallelization for Multi-DSPs
Material kindly made available by
Björn Franke and Michael O’Boyle University of Edinburgh, UK School of Informatics

## Slide 39: Parallelization for Multi-DSPs
Motivation
Performance demands of complex systems often exceed capabilities of a single processor (e.g., radar, sonar, medical image processing, HDTV, ...)
Multiple DSPs operating in parallel provide enough performance, but...
  little or no hardware support for the parallel execution of software
  even less support of parallel programming paradigms by development tools
  existing source codes are often written in low-level style which impedes an effective parallelization

## Slide 40: Parallelizing Compilers
Research Area “High-Performance Computing”
Research on vectorizing compilers for more than 40 years
Traditionally Fortran compilers
These vectorizing compilers are usually not suitable for Multi-DSPs, since their assumptions on the memory hierarchy are unrealistic:
  Communication between processes via shared memory
  Memory has only one single, shared address space
  Caches can be local and/or shared, but cache coherence issues are solved in hardware
 De facto no parallelizing compilers available for Multi-DSPs

## Slide 41: Multi-DSPs
DSP Core 0
Mem
Bank 1
Mem
Bank 2
DSP Core X
Mem
Bank 1
Mem
Bank 2
External
Memory
<Int 1, 100>
Bus
<Int 2, 100>
<Ext, 100>
<Remote X1, 100>
Several address spaces: Internal 1 & 2, external, remote DSP core
Use of internal memories: High bandwidth, low access latencies
Use of remote memories: ID of remote DSPs must be known

## Slide 42: Workflow of Parallelization
Program Recovery
Removal of undesired low-level constructs from code
Replacement by high-level constructs
Detection of Parallelism
Identification of loops amenable for parallelization
Partitioning and Allocation of Data
Minimization of communication overhead between DSPs
Locality Improvement of Memory Accesses
Minimization of accesses to memories of remote DSPs
Optimization of Memory Transfers
Use of DMA for burst transfers

## Slide 43: Code Example for 2 parallel DSPs
/* Array declarations */
int A[16], B[16], C[16], D[16];
/* Declaration & initialization of pointers */
int *p_a = A, *p_b = &B[15], *p_c = C, *p_d = D;
/* Loop over all array elements */
for (i = 0; i < 16; i++)
*p_d++ = *p_c++ + *p_a++ * *p_b--;
Low-level array accesses via pointers; explicit pointer arithmetic ( cf. chapter 2, auto-increment addressing)
Disadvantageous for parallelization since ad hoc no structure in array accesses visible and analyzable
*p_d++ = *p_c++ + *p_a++ * *p_b--;

## Slide 44: Program Recovery
/* Array declarations */
int A[16], B[16], C[16], D[16];
/* Loop over all array elements */
for (i = 0; i < 16; i++)
D[i] = C[i] + A[i] * B[15-i];
Replacement of pointer accesses by explicit array operators [ ]
Structure of array accesses better visible, more amenable for subsequent analyses

## Slide 45: Program Recovery
/* Array declarations */
int A[16], B[16], C[16], D[16];
/* Loop over all array elements */
for (i = 0; i < 16; i++)
D[i] = C[i] + A[i] * B[15-i];
One-dimensional “flat” arrays too unstructured for parallelization for Multi-DSPs
Partitioning of arrays onto available parallel DSPs unclear

## Slide 46: Data Partitioning
/* Partitioned array declarations */
int A[2][8], B[2][8], C[2][8], D[2][8];
/* Loop over all array elements */
for (i = 0; i < 16; i++)
D[i/8][i%8] = C[i/8][i%8] +
A[i/8][i%8] * B[(15-i)/8][(15-i)%8];
New, two-dimensional array declarations
First dimension equals number of available parallel DSPs
Original flat arrays now partitioned in disjoint areas that can be processed independently from each other

## Slide 47: Data Partitioning
/* Partitioned array declarations */
int A[2][8], B[2][8], C[2][8], D[2][8];
/* Loop over all array elements */
for (i = 0; i < 16; i++)
D[i/8][i%8] = C[i/8][i%8] +
A[i/8][i%8] * B[(15-i)/8][(15-i)%8];
Extremely costly and complex addressing required
Reason: Arrays are multi-dimensional; loop index variable i used to index the arrays is purely sequential

## Slide 48: Strip Mining of i-Loop
/* Partitioned array declarations */
int A[2][8], B[2][8], C[2][8], D[2][8];
/* Nested loop over all array elements */
for (j = 0; j < 2; j++)
for (i = 0; i < 8; i++)
D[j][i] = C[j][i] + A[j][i] * B[1-j][7-i];
Splitting of sequential iteration space of i into two independent, two-dimensional iteration spaces
Iteration spaces of new loop nest now matches nicely with data layout
Only affine expressions for array accesses

## Slide 49: Strip Mining of i-Loop
/* Partitioned array declarations */
int A[2][8], B[2][8], C[2][8], D[2][8];
/* Nested loop over all array elements */
for (j = 0; j < 2; j++)
for (i = 0; i < 8; i++)
D[j][i] = C[j][i] + A[j][i] * B[1-j][7-i];
How can this code be parallelized for two DSPs?

## Slide 50: Parallelization (for Processor 0)
/* Definition of the processor ID */
#define MYID 0
/* Partitioned array declarations */
int A[2][8], B[2][8], C[2][8], D[2][8];
/* Simple loop over all array elements for DSP No. MYID */
for (i = 0; i < 8; i++)
D[MYID][i] = C[MYID][i] + A[MYID][i] * B[1-MYID][7-i];
Insertion of an explicit processor ID
Array accesses now make use of processor ID
For N parallel processors, N different HIR codes are generated each of which with a unique processor ID

## Slide 51: Parallelization (for Processor 0)
/* Definition of the processor ID */
#define MYID 0
/* Partitioned array declarations */
int A[2][8], B[2][8], C[2][8], D[2][8];
/* Simple loop over all array elements for DSP No. MYID */
for (i = 0; i < 8; i++)
D[MYID][i] = C[MYID][i] + A[MYID][i] * B[1-MYID][7-i];
This structure makes explicit which code will run on which DSP
It still remains unclear how the arrays are distributed onto local memory banks or on external memories, and how accesses to memory banks of remote DSPs happen

## Slide 52: Array Descriptors
Two-dimensional array A[2][8] is partitioned into two sub-arrays A0 and A1 along the first dimension
Each sub-array An is assigned to the memory of processor n
Original, two-dimensional array accesses need to be re-directed towards A0 and A1 using array descriptors
Sub-Array
A0[0...7]
A0 | A1
DSP 0
Sub-Array
A1[0...7]
A0 | A1
DSP 1
Array Descriptors
A[0][5]
A[0][5]

## Slide 53: Memory Assignment (for Processor 0)
Array accesses via descriptors in unchanged syntax
/* Definition of the processor ID */
#define MYID 0
/* Partitioned array declarations & array descriptors */
int A0[8]; extern int A1[8]; int *A[2] = { A0, A1 };
int B0[8]; extern int B1[8]; int *B[2] = { B0, B1 }; ...
/* Simple loop over all array elements for DSP No. MYID */
for (i = 0; i < 8; i++)
D[MYID][i] = C[MYID][i] + A[MYID][i] * B[1-MYID][7-i];
Arrays in DSP-internal and remote memories

## Slide 54: Memory Assignment (for Processor 0)
Descriptor access to local arrays inefficient due to additional indirection
Scheduling problems: A[i][j] can have varying access latency if i references local or remote memory
/* Definition of the processor ID */
#define MYID 0
/* Partitioned array declarations & array descriptors */
int A0[8]; extern int A1[8]; int *A[2] = { A0, A1 };
int B0[8]; extern int B1[8]; int *B[2] = { B0, B1 }; ...
/* Simple loop over all array elements for DSP No. MYID */
for (i = 0; i < 8; i++)
D[MYID][i] = C[MYID][i] + A[MYID][i] * B[1-MYID][7-i];

## Slide 55: Locality Improvement for Array Accesses
Direct accesses to local arrays; refrain from accesses via descriptors whenever possible
Maximal exploitation of high bandwidths of local memories
/* Definition of the processor ID */
#define MYID 0
/* Partitioned array declarations & array descriptors */
int A0[8]; extern int A1[8]; int *A[2] = { A0, A1 };
int B0[8]; extern int B1[8]; int *B[2] = { B0, B1 }; ...
/* Simple loop over all array elements for DSP No. MYID */
for (i = 0; i < 8; i++)
D0[i] = C0[i] + A0[i] * B[1-MYID][7-i];

## Slide 56: Locality Improvement for Array Accesses
8 sequential accesses to consecutive array elements in remote memory
Inefficient, since 8 full bus cycles are required
/* Definition of the processor ID */
#define MYID 0
/* Partitioned array declarations & array descriptors */
int A0[8]; extern int A1[8]; int *A[2] = { A0, A1 };
int B0[8]; extern int B1[8]; int *B[2] = { B0, B1 }; ...
/* Simple loop over all array elements for DSP No. MYID */
for (i = 0; i < 8; i++)
D0[i] = C0[i] + A0[i] * B[1-MYID][7-i];

## Slide 57: Insertion of DMA Burst Transfers
/* Definition of the processor ID */
#define MYID 0
/* Partitioned array declarations & array descriptors */
int A0[8]; extern int A1[8]; int *A[2] = { A0, A1 };
int B0[8]; extern int B1[8]; int *B[2] = { B0, B1 }; ...
/* Temporary DMA buffer */
int temp[8];
DMA_get( temp, &(B[1-MYID]), 8 * sizeof( int ) );
/* Simple loop over all array elements for DSP No. MYID */
for (i = 0; i < 8; i++)
D0[i] = C0[i] + A0[i] * temp[7-i];
Block-wise loading of a local buffer from remote memory via DMA
Array accesses in loop use only local memory

## Slide 58: Experimental Setup
Multi-DSP Hardware
4 parallel Analog Devices TigerSHARC TS-101 @250 MHz
768 kB local SRAM per DSP, 128 MB external DRAM
Parallelized Benchmark Programs
DSPstone: small DSP kernels, low code complexity
UTDSP: complex applications, compute-intensive code
Results: Run-times
for purely sequential code running on 1 DSP
for code after program recovery
for code after data partitioning and memory assignment
for code after locality improvement & DMA

## Slide 59: Results – DSPstone
Chart: Speedup
| convolution | fir | fir2dim | lms | matrix1 | matrix2 | n_complex_updates | n_real_updates
Sequential | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Program Recovery | 1 | 0.41711 | 1.7193 | 1.2 | 1 | 1.6694 | 1 | 1
Partitioning & Allocation | 1.8837 | 0.58393 | 1.2437 | 0.99071 | 0.044665 | 0.013628 | 0.75542 | 0.31104
Locality & DMA | 3.5629 | 1.9304 | 5.413 | 5.0487 | 4.0005 | 6.5074 | 3.9887 | 3.8125

## Slide 60: Results – UTDSP

## Slide 61: Discussion
Mean Overall Speedups
DSPstone: 4.06x
UTDSP: 3.38x
All benchmarks: 3.68x
Very Astonishing
How is it possible to achieve (mean) speedups of a factor of 4 for DSPstone if parallelization is done for 4 DSPs?

## Slide 62: Reasons for Over-Proportional Speedups
Over-Proportional Speedups > 4 for 4 parallel DSPs
Parallelized code is more amenable for subsequent compiler optimizations than original sequential code
Example: Sequential i-loop ( cf. Slide 47): 16 iterations i-loop parallelized for 2 DSPs (Slide 49): 8 iterations
Parallelized loops possibly candidates for Loop Unrolling:
Fully unrolled loop without any branches!
No delay slots, no potential for branch misprediction
for (i = 0; i < 8; i++)
<loop body>;
<loop body>;
<loop body>;
...
<loop body>;
8 times

## Slide 63: References
Function Specialization
D. Bacon, S. Graham, O. Sharp. Compiler Transformations for High-Performance Computing. ACM Computing Surveys 26(4), 1994. (Excellent survey paper on compiler optimizations in general!)
P. Lokuciejewski, H. Falk, H. Theiling. Influence of Procedure Cloning on WCET Prediction. CODES+ISSS, Salzburg 2007.
Parallelization for Homogeneous Multi-DSPs
B. Franke, M. O´Boyle. A Complete Compiler Approach to Auto-Parallelizing C Programs for Multi-DSP Systems. IEEE Transactions on Parallel and Distributed Systems 16(3), 2005.

## Slide 64: Summary
HIR Optimizations
Restructuring of Loops
Restructuring of functions and their calling relationships
Function Specialization / Procedure Cloning
Specialization of general-purpose functions
Enable standard optimizations within specialized functions, simplify code for parameter passing
Impact on ACET marginal, but huge for WCETEST
Parallelization for Homogeneous Multi-DSPs
Focus on exploitation of local memories and address ranges
Speedups mostly linear in the number of available parallel DSPs