## Slide 1: Compilers for Embedded Systems
Summer Term 2022
Heiko Falk
Institute of Embedded Systems
Electrical Engineering, Computer Science and Mathematics
Hamburg University of Technology

## Slide 2: Chapter 9 WCET-Aware Compilation

## Slide 3: Outline
Introduction & Motivation
Compilers for Embedded Systems – Requirements & Dependencies
Internal Structure of Compilers
Pre-Pass Optimizations
HIR Optimizations and Transformations
Code Generation
LIR Optimizations and Transformations
Register Allocation
WCET-Aware Compilation
Outlook

## Slide 4: Chapter Contents
WCET-Aware Compilation
  Introduction
    Integration of a WCET Timing Model into a Compiler
    Challenges for WCET-Aware Optimization
  Procedure Cloning & Positioning
    WCET-Aware Procedure Cloning
    Procedure Positioning for Cache Miss Reduction
  Register Allocation
    Problem of Classical Graph Coloring
    WCET-Aware Graph Coloring
  Scratchpad Allocation of Data and Code
    Allocation of global Data
    Allocation of Basic Blocks

## Slide 5: Software Design for Real-Time Systems
Current Industrial Practice (Automotive, Avionics)
Specification using graphical / high-level tools
Automatic generation of ANSI-C code
Compilation of binary machine code for a given processor architecture
Repeated executions / simulations of generated machine code, usage of “representative” input data
Time measurements provide “observed execution times”
Addition of safety margin (e.g., 20%) to greatest observed execution time: “observed Worst-Case Execution Time”
Observed WCET ≤ Real-time constraint? No: Go to 1

## Slide 6: Problems of this Design Flow
Safety
No guarantee that observed WCET (even only approximately) matches the actual WCET
No guarantee that a real-time system always terminates in time
Design Time
How many iterations are required until step 7 successful?
Depends on in how far steps 2-3 lead to the effective acceleration of the generated code in the worst case
Try & Error until step 7 successful

## Slide 7: Current State of the Art in Compiler Construction
Objective Function of Compiler Optimizations
Usually reduction of Average-Case Execution Times (ACET): Accelerate a “typical” execution of a program using “typical” input data
No statements about the impact of optimizations on WCETs possible
Optimization Strategy
Naive: Current compilers lack precise ACET timing model
Application of an optimization if “promising”
ACET-related effects of optimizations unknown to compiler
ACET optimizations potentially increase WCETs – Compilers often invoked without any optimizations for real-time systems

## Slide 8: Motivation
Design of a Compiler that
considers WCETEST instead of average-case runtimes,
allows formal guarantees on worst-case properties, instead of relying on observed execution times,
applies fully automated optimizations to minimize WCETEST
Approach
Integration of a WCETEST timing model into compiler by coupling compiler back-end with static WCET analyzer.
Exploitation of WCETEST timing model by novel optimizations explicitly aiming at WCETEST minimization.

## Slide 9: Integration of WCETEST Model into Compiler (1)
Re-implementation of a WCET timing model in compiler makes no sense
Instead: Tight integration of aiT ( chapter 5)
Coupling inside processor-specific compiler back-end (LLIR)
Seamless exchange of information via translation LLIR  CRL2
Transparent invocation of aiT inside the compiler
Import of WCET-related data into compiler back-end

## Slide 10: Integration of WCETEST Model into Compiler (2)
Relevant WCET data:
WCETEST of entire program, function or basic block
Worst-case execution frequency per function, basic block or CFG edge
Potential register contents
Cache Hits / Misses per basic block

## Slide 11: WCC – The WCET-aware C Compiler (1)
Flow Facts
WCET analysis: max. iteration counts & recursion depths
WCC: Annotation directly in C source code: _Pragma( ”loopbound min 10 max 10” );
Automatic flow fact update during control flow-modifying optimizations

## Slide 12: WCC – The WCET-aware C Compiler (2)
Loop Analyzer
Manual annotation of Flow Facts tedious and error-prone
WCC: Automated loop analysis that determines maximal iteration counts
Partially bases on polyhedral models ( chapter 4)

## Slide 13: WCC – The WCET-aware C Compiler (3)
Back-Annotation
WCETEST data of aiT only available in back-end
HIR optimizations have no accesses to WCETEST data
WCETEST minimization at HIR level impossible
WCC: Back-annotation translates WCETEST data from LIR to HIR

## Slide 14: WCC – The WCET-aware C Compiler (4)
Memory Hierarchy
aiT operates on binary code using physical addresses
WCC must provide correct physical addresses for code, data, branches and load/store operations to aiT
WCC requires detailed knowledge about memories

## Slide 15: WCC – The WCET-aware C Compiler (5)
Memory Hierarchy
Memory regions, their start addresses, sizes, access latencies, access attributes (code, data, read-/writable, ...)
SPM allocations also require this information for their optimizations

## Slide 16: WCC – The WCET-aware C Compiler (6)
Memory Hierarchy
WCC decides on memory layout of code and data but produces no binary code
Linker must generate binary code in strict compliance with WCC’s memory layout
WCC: Automatic generation of an adapted linker script
[http://www.tuhh.de/es/esd/research/wcc]

## Slide 17: Challenges during WCETEST Minimization
The Worst-Case Execution Path (WCEP)
WCET of a program = Length of the program’s longest execution path (WCEP)
WCETEST minimization: Optimization of only those parts of a program lying on the WCEP
Code optimization apart the WCEP will not reduce WCETEST
Optimizations minimizing WCETEST require detailed knowledge of the WCEP!
WCET analyzer aiT provides such detailed information by means of execution frequencies of CFG edges. But...

## Slide 18: Instability of the WCEP (1)
main
a
b
c
d
10 Cyc.
50 Cyc.
80 Cyc.
65 Cyc.
120 Cyc.
WCETEST of
basic block a
Example: Simple CFG with 5 basic blocks

## Slide 19: Instability of the WCEP (2)
main
a
b
c
d
10 Cyc.
50 Cyc.
80 Cyc.
65 Cyc.
120 Cyc.
Initial WCEP: main, a, b, c
Length of WCEP = WCETEST = 205
In the following: Optimization of b
WCETEST = 205 Cyc.

## Slide 20: Instability of the WCEP (3)
main
a
c
d
10 Cyc.
50 Cyc.
80 Cyc.
65 Cyc.
120 Cyc.
Initial WCEP: main, a, b, c
Length of WCEP = WCETEST = 205
In the following: Optimization of b
WCETEST = 205 Cyc.
b
40

## Slide 21: Instability of the WCEP (4)
main
a
c
d
10 Cyc.
50 Cyc.
80 Cyc.
65 Cyc.
120 Cyc.
Novel WCEP: main, d, c
Novel WCETEST: 195
WCEP has changed due to an optimization!
b
40
WCETEST = 195 Cyc.

## Slide 22: Consequences for Compiler Optimizations
WCET-Aware Optimizations...
... always have to be aware that the WCEP can change after each individual optimization decision.
... should take the decision where to optimize something not only based on local information, but should always consider the global effects of an optimization decision. (The optimization of b in the previous example locally reduces the WCETEST of b by 40 cycles. But globally, only 10 cycles were saved!)
 Challenge: To design novel compiler optimizations that fulfill the above requirements and that always consider the entire CFG and the current WCEP therein.

## Slide 23: Chapter Contents
WCET-Aware Compilation
  Introduction
    Integration of a WCET Timing Model into a Compiler
    Challenges for WCET-Aware Optimization
  Procedure Cloning & Positioning
    WCET-Aware Procedure Cloning
    Procedure Positioning for Cache Miss Reduction
  Register Allocation
    Problem of Classical Graph Coloring
    WCET-Aware Graph Coloring
  Scratchpad Allocation of Data and Code
    Allocation of global Data
    Allocation of Basic Blocks

## Slide 24: Why Procedure Cloning and WCETEST?
Motivation ( cf. chapter 5)
Frequent occurrences of general-purpose functions in special-purpose contexts in embedded software
Loop bounds are particularly often controlled by function parameters
Loop bounds are particularly critical for WCET estimates
Procedure Cloning allows the extremely precise annotation of loop bounds for WCET analysis
[P. Lokuciejewski. Influence of Procedure Cloning on WCET Prediction. CODES+ISSS, Salzburg, 2007]

## Slide 25: Results after Classical Cloning
Chart: Rel. WCETEST [%]
| TriCore | ARM | Thumb
EPIC | 0.0539 | 0.0428 | 0.0435
MPEG2 | 0.7008 | 0.6675 | 0.6655
GSM | 0.8186 | 0.8727 | 0.6897
Geo. Mean | 0.31387 | 0.29214 | 0.27129
Chart: Rel. Code Size [%]
| TriCore | ARM | Thumb
EPIC | 3.2657 | 3.0505 | 3.2975
MPEG2 | 1.2894 | 1.2336 | 1.22
GSM | 1.019 | 1.0328 | 1.0314
Geo. Mean | 1.625 | 1.5722 | 1.6069
WCETEST improvements from 13% up to 95%!
Code size increases from 2% up to 325%!

## Slide 26: Key Problems of Classical Cloning
WCETEST of a program corresponds to length of WCEP
Classical Procedure Cloning is fully unaware of WCEP
Properties of functions that potentially yield WCETEST reductions (parameter-dependent loops) are not considered by the classical standard optimization
Potential cloning of functions that do not lie on the WCEP
Potential cloning of functions that do not contribute to a WCETEST reduction
Unnecessary code size increases without any benefit in terms of WCETEST reduction

## Slide 27: WCET-aware Cloning (1)
Input
Program P to be optimized, given in the form of an HIR
Float value maxFactor that denotes the maximally acceptable code size increase
Initialization
maxCodeSize = getCodeSize( P ) * maxFactor;
Phase 1 – Determination of the WCEP
Perform a WCET analysis of P;
Determine set F of all original functions lying on the WCEP of P;
wcetorig = getWCET( P );
csorig = getCodeSize( P );

## Slide 28: WCET-aware Cloning (2)
Phase 2 – Determination of WCETEST Data per Function
for ( <all functions f  F> )
if ( <f is called with constant value as some parameter p> &&
( <p is used as loop bound> ||
<p is used in a condition of an if-statement> ||
<p is argument in some other function call inside f> ) )
// Cloning of f eventually beneficial w.r.t. WCETEST
HIR P’ = P.copy();
doCloning( P’, f ); // Try out cloning of f
updateLoopBounds( P’, f );
deleteRedundantIfStmts( P’, f );
Perform WCET analysis of P’;
wcetf = getWCET( P’ );
csf = getCodeSize( P’ );

## Slide 29: WCET-aware Cloning (3)
Phase 3 – Determination of that Function with highest Profit
for ( <all functions f  F> )
profitf = ( wcetorig – wcetf ) / ( csf – csorig );
Determine function fopt with maximal profitf AND
csf ≤ maxCodeSize;
if ( <fopt exists> )
doCloning( P, fopt );
goto <Phase 1>;
[P. Lokuciejewski. WCET-Driven, Code-Size Critical Procedure Cloning. SCOPES, Munich, 2008]

## Slide 30: Relative WCETEST after WCET-aware Cloning
100% = WCETEST without any procedure cloning
WCETEST reductions from 14% up to 64%!

## Slide 31: Relative Code Sizes after WCET-aware Cloning
100% = Code size without any procedure cloning
Code size increase of EPIC: 190% instead of 300%

## Slide 32: Eviction of Code from Instruction Caches
Caches exploit locality of memory accesses
  Spatial Locality: Memory accesses target a spatially small memory region that should be kept in the cache completely
  Temporal Locality: In a short period of time, spatially scattered memory regions are accessed so that these regions should be kept in the cache
Poor layout of code (or data) in memory can lead to a bad cache performance if temporal locality is high:
Scattered memory regions with high temporal locality can, when arranged badly in memory, evict themselves repeatedly from the cache, thus yielding many cache misses – so-called conflict misses.

## Slide 33: Example of I-Cache Evictions (1)
foo1
foo2
foo3
Main Memory
I-Cache
Way 0
Way 1
foo1
foo2
foo3
0
1
2
3
4
5
6
S
...
0
1
2
3
4
5
6
S
...
Set
...
...
...
0
1
2
3
4
5
S
...
Set
0
1
2
3
4
5
S
...
0
1
2
void foo1() {
for (i=0; i<n; i++) {
foo2();
foo3();
// More Code
}
}
Here: 2-way set-associative
I-Cache
foo1

## Slide 34: Example of I-Cache Evictions (2)
foo1
foo2
foo3
I-Cache
Way 0
Way 1
foo1
foo2
foo3
0
1
2
3
4
5
6
S
...
0
1
2
3
4
5
6
S
...
Set
...
...
...
0
1
2
3
4
5
S
...
Set
0
1
2
3
4
5
S
...
0
1
2
foo1
foo2
void foo1() {
for (i=0; i<n; i++) {
foo2();
foo3();
// More Code
}
}
Here: 2-way set-associative
I-Cache
Main Memory

## Slide 35: Example of I-Cache Evictions (3)
foo1
foo2
foo3
I-Cache
Way 0
Way 1
foo1
foo2
foo3
0
1
2
3
4
5
6
S
...
0
1
2
3
4
5
6
S
...
Set
...
...
...
0
1
2
3
4
5
S
...
Set
0
1
2
3
4
5
S
...
0
1
2
foo1
foo2
foo3
void foo1() {
for (i=0; i<n; i++) {
foo2();
foo3();
// More Code
}
}
Here: 2-way set-associative
I-Cache
Main Memory

## Slide 36: Example of I-Cache Evictions (4)
foo1
foo2
foo3
I-Cache
Way 0
Way 1
foo1
foo2
foo3
0
1
2
3
4
5
6
S
...
0
1
2
3
4
5
6
S
...
Set
...
...
...
0
1
2
3
4
5
S
...
Set
0
1
2
3
4
5
S
...
0
1
2
foo1
foo2
foo3
void foo1() {
for (i=0; i<n; i++) {
foo2();
foo3();
// More Code
}
}
Here: 2-way set-associative
I-Cache
Main Memory

## Slide 37: A better Memory Layout without Evictions (1)
foo1
foo2
foo3
I-Cache
Way 0
Way 1
foo1
foo2
foo3
0
1
2
3
4
5
6
S
...
0
1
2
3
4
5
6
Set
...
...
0
1
2
3
4
5
7
Set
8
9
S
...
0
1
2
7
8
9
6
foo1
void foo1() {
for (i=0; i<n; i++) {
foo2();
foo3();
// More Code
}
}
Here: 2-way set-associative
I-Cache
Main Memory

## Slide 38: A better Memory Layout without Evictions (2)
foo1
foo2
foo3
I-Cache
Way 0
Way 1
foo1
foo2
foo3
0
1
2
3
4
5
6
S
...
0
1
2
3
4
5
6
Set
...
...
0
1
2
3
4
5
7
Set
8
9
S
...
0
1
2
7
8
9
6
foo1
foo2
void foo1() {
for (i=0; i<n; i++) {
foo2();
foo3();
// More Code
}
}
Here: 2-way set-associative
I-Cache
Main Memory

## Slide 39: A better Memory Layout without Evictions (3)
foo1
foo2
foo3
I-Cache
Way 0
Way 1
foo1
foo2
foo3
0
1
2
3
4
5
6
S
...
0
1
2
3
4
5
6
Set
...
...
0
1
2
3
4
5
7
Set
8
9
S
...
0
1
2
7
8
9
6
foo1
foo2
foo3
void foo1() {
for (i=0; i<n; i++) {
foo2();
foo3();
// More Code
}
}
Here: 2-way set-associative
I-Cache
Main Memory

## Slide 40: A better Memory Layout without Evictions (4)
foo1
foo2
foo3
I-Cache
Way 0
Way 1
foo1
foo2
foo3
0
1
2
3
4
5
6
S
...
0
1
2
3
4
5
6
Set
...
...
0
1
2
3
4
5
7
Set
8
9
S
...
0
1
2
7
8
9
6
foo1
foo2
foo3
void foo1() {
for (i=0; i<n; i++) {
foo2();
foo3();
// More Code
}
}
Here: 2-way set-associative
I-Cache
Main Memory

## Slide 41: Procedure Positioning using Call Graphs
Definition (Call Graph):
The Call Graph is an undirected weighted graph G = (V, E, w) with
V contains a node v per function of a program
E contains an edge e = {v, w} if a function v calls function w
Each edge e = {v, w} is weighted with the frequency w(e) how often v and w call themselves
Concept of WCET-aware Procedure Positioning
Generate call graphs with edge weights equal to worst-case call frequencies as determined during static WCET analysis
Repeatedly place two functions with high edge weights consecutively in memory

## Slide 42: WCET-aware Procedure Positioning (1)
Input
Program P to be optimized, given in the form of an LIR
Initialization
Perform a WCET analysis of P;
Generate call graph Gorig = (Vorig, Eorig, worig) of P based on WCET data;
Generate call graph Gnew = (Vnew, Enew, wnew) = Gorig.copy();
[P. Lokuciejewski et al. WCET-driven Cache-based Procedure Positioning Optimizations. ECRTS, Prague, 2008]

## Slide 43: WCET-aware Procedure Positioning (2)
Optimization Loop
do
wcetcurrent = getWCET( P );
for ( <all edges e = {v, w}  Enew, sorted in descending order w.r.t. wnew> )
if ( Positioning( e, Gnew, Gorig, P, wcetcurrent ) == true )
// If contiguous placement of nodes v and w in memory reduces
// WCETEST, terminate for-loop and continue with do-while-loop.
break;
while ( <P was modified during last iteration> );

## Slide 44: WCET-aware Procedure Positioning (3)
Positioning( e = {v, w}  Enew, Gnew, Gorig, P, wcetcurrent )
Generate LIR P’ with v and w placed contiguously in memory;
Perform a WCET analysis of P’;
wcetnew = getWCET( P’ );
if ( wcetnew < wcetcurrent )
P = P’;
Merge nodes v and w in Gnew;
Update wnew based on novel WCET data;
return true;
else
return false;

## Slide 45: Merging of Nodes
Contiguous Placement of merged Nodes in Memory
Problem: How shall (A, B) and (D, E) be placed in the next step?
Gorig reveals that A and D should be placed contiguously
Best placement is (B, A, D, E).
That’s why Gorig is kept throughout the positioning algorithm!
D
C
B
E
A
4
1
2
3
8
6
D
C
A,B
E
4
1
5
6
D,E
C
A,B
4
1
5
Gorig
Gnew

## Slide 46: Properties
Algorithm greedily places two nodes of the current graph Gnew contiguously in memory in one iteration
Here, always those two nodes are considered which call themselves most frequently according to wnew
Instable WCEPs are considered by the algorithm, because a WCET analysis is done for each placement, and because the edge weights wnew are updated according to this novel WCET data
Since WCET-aware Procedure Cloning places the novel clones at the end of a program, it makes sense to combine WCET-aware Cloning and Positioning

## Slide 47: Relative WCETEST after WCET-Cloning & Positioning
100% = WCETEST w/o Procedure Cloning and Positioning
I-Cache: 16kB, 2-way set-associative, LRU replacement
WCET-Positioning of clones: additional WCETEST reduction by up to 7% compared to cloning w/o positioning
Chart: Relative WCET [%]
| expint | g721 enc. | g723 enc. | gsm dec. | gsm enc. | mpeg2 | Geo. Mean
Cloning w/o Positioning | 0.401 | 0.894 | 1 | 0.358 | 0.592 | 0.5516 | 0.58937
Cloning with Positioning | 0.399 | 0.8151 | 0.932 | 0.3541 | 0.5783 | 0.4839 | 0.55754
Caution: Don’t compare this diagram with slide 30, since I-cache was disabled in slide 30!

## Slide 48: Conclusions
Comparison with Consequences for WCETEST Optimizations
WCET-aware optimizations...
... mandatorily need detailed knowledge of the WCEP
WCET-Cloning and WCET-Positioning both consider the WCEP
... always have to be aware that the WCEP can change after each individual optimization decision
Both optimizations update the WCEP after each modification of the code
... should take the decision where to optimize something not only based on local information, but should always consider the global effects of an optimization decision
WCET-Cloning and WCET-Positioning are both greedy heuristics that are driven solely by local data per function

## Slide 49: Chapter Contents
WCET-Aware Compilation
  Introduction
    Integration of a WCET Timing Model into a Compiler
    Challenges for WCET-Aware Optimization
  Procedure Cloning & Positioning
    WCET-Aware Procedure Cloning
    Procedure Positioning for Cache Miss Reduction
  Register Allocation
    Problem of Classical Graph Coloring
    WCET-Aware Graph Coloring
  Scratchpad Allocation of Data and Code
    Allocation of global Data
    Allocation of Basic Blocks

## Slide 50: Register Allocation by Graph Coloring
Build: Create interference graph G = (V, E) with V = {virtual registers} ∪ {K physical processor registers}, e = (v, w) ∈ E  VREGs v and w may never share the same PHREG, i.e. v and w interfere
Simplify: Remove all nodes v ∈ V with degree < K
Spill: After step 2, each node of G has degree ≥ K. Select one node v ∈ V; mark v as potential spill; remove v from G
Repeat Simplify and Spill until G = Ø
Select: Re-insert nodes v into G in reverse order; if there is a free color kv, color v; otherwise, mark v as actual spill
Generate Spill Code before/after actual spills; go to step 1 if #VREGS > 0
[A. W. Appel. Modern compiler implementation in C. 2004]

## Slide 51: Problem of Standard Graph Coloring
Spill: After step 2, each node of G has degree ≥ K. Select one node v ∈ V; mark v as potential spill; remove v from G
Which node v should be selected as potential spill?
Common graph coloring implementations select ...
    ... the first node v according to the order in which VREGs were generated during code generation,
    ... the node with highest degree in the interference graph,
    ... a node with high degree, with few DEFs/USEs, not in some inner loop – maybe depending on profiling data.
Uncontrolled spill code generation – potentially along Worst-Case Execution Path (WCEP) defining the WCET!

## Slide 52: A Chicken-Egg Problem
A WCET-aware Register Allocator...
... relies on WCET data provided by WCET analysis using aiT,
... but cannot obtain WCET data since code containing virtual registers is not executable and thus not analyzable!
The Way Out
Start by marking all VREGs as actual spill  Code has lousy quality, but is fully analyzable
Perform WCET analysis, get WCEP P
Apply standard graph coloring to all VREGs of that basic block b ∈ P with most executions of spill code in the worst case
Re-evaluate novel WCEP

## Slide 53: WCET-aware Graph Coloring (1)
LLIR WCET_GC_RA( LLIR P )
{
// Iterate until current WCEP is fully allocated.
while ( true )
{
// Copy P, spill all VREGs of P’ onto stack.
LLIR P’ = P.copy();
P’.spillAllVREGs();
// Compute Worst-Case Execution Path for fully spilled LIR.
set<basic_blocks> WCEP = computeWCEP( P’ );
// If there are no more VREGs, the allocation loop is over.
if ( getVREGs( WCEP ) ==  )
break;

## Slide 54: WCET-aware Graph Coloring (2)
// Determine that block on the WCEP with highest product of
// Worst-Case Execution Count * spilling instructions.
basic_block b’ = getMaxSpillCodeBlock( WCEP );
basic_block b = getBlockOfOriginalP( b’ );
// Collect all VREGs of this most critical block.
list<virtualRegister> vregs = getVREGs( b );
// Sort VREGs by #occurrences, apply standard graph coloring.
vregs.sort( occurrences of VREG in b );
traditionalGraphColoring( P, vregs );
}
// Allocate all remaining VREGs not lying on the WCEP.
traditionalGraphColoring( P, getVREGs( P ) );
return P;
}

## Slide 55: Properties (1)
Algorithm simultaneously handles a program P to be register allocated, and a copy P’ where all VREGs are completely spilled to memory in order to enable WCET analysis.
Register allocation is done basic block-wise along the WCEP.
After the allocation of one basic block, the WCEP in P’ is recomputed.
In one iteration of the algorithm: Allocation of all VREGs occurring in that basic block b that contains many spill instructions in P’ and that is executed very often.
The VREGs of this most timing-critical block b should be kept in PHREGs if possible.

## Slide 56: Properties (2)
Spilling of VREGs in b cannot be avoided in general. If spilling is required in b, spill only those VREGs v of b that occur least frequently in b, since few occurrences of v in b imply few spill instructions inside b.
Register allocation itself, i.e., assigning colors to b’s VREGs, and spill code generation are handed over to standard graph coloring.
After the allocation loop, the WCEP is completely allocated. But there may still be some VREGs in blocks besides the WCEP.
One final run of standard graph coloring in order to catch all those remaining VREGs.
[H. Falk. WCET-aware Register Allocation based on Graph Coloring. DAC, San Francisco, 2009]

## Slide 57: Relative WCETEST after WCET-aware Graph Coloring
Chart: Relative WCET [%] (Optimization Level -O3)
| adpcm_verify | cjpeg_transupp | compress | crc | dijkstra | duff | edge_detect | edn | epic | expint | fdct | fft_1024 | fft_256 | fir | fir2dim | gsm | gsm_encode | h263 | h264dec_block | h264dec_macro | iir_4_64 | iir_biquad_N | jfdctint | latnrm_32_64 | lmsfir_8_1 | lmsfir_32_64 | lpc | ludcmp | matmult | matrix2_fixed | matrix2_float | md5 | minver | mult_10_10 | mult_4_4 | ndes | prime | qmf_receive | qmf_transmit | qurt | rijndael_enc | select | sha | spectral | startup | v32_benc | Geo. Mean
Relative WCET | 0.7881 | 0.5899 | 0.4002 | 0.8646 | 0.4179 | 0.4859 | 0.6501 | 0.9249 | 0.2712 | 0.6916 | 0.7896 | 0.5483 | 0.5765 | 0.6906 | 0.8568 | 0.4848 | 0.338 | 0.7909 | 0.8453 | 0.7429 | 0.5789 | 0.886 | 0.7694 | 0.8461 | 0.7868 | 0.7734 | 0.8507 | 0.6629 | 0.5441 | 0.7059 | 0.7598 | 0.6513 | 0.8662 | 0.6079 | 0.7378 | 0.7761 | 0.8758 | 0.6265 | 0.6818 | 0.9305 | 0.816 | 0.6583 | 0.6422 | 0.241 | 0.694 | 0.9298 | 0.66118
100% = WCETEST using Standard Graph Coloring (highest degree)
93%
24%
66%

## Slide 58: Relative ACET after WCET-aware Graph Coloring
Chart: Relative ACET [%] (Optimization Level -O3)
| adpcm_verify | cjpeg_transupp | compress | crc | dijkstra | duff | edge_detect | edn | epic | expint | fdct | fft_1024 | fft_256 | fir | fir2dim | gsm | gsm_encode | h263 | h264dec_block | h264dec_macro | iir_4_64 | iir_biquad_N | jfdctint | latnrm_32_64 | lmsfir_8_1 | lmsfir_32_64 | lpc | ludcmp | matmult | matrix2_fixed | matrix2_float | md5 | minver | mult_10_10 | mult_4_4 | ndes | prime | qmf_receive | qmf_transmit | qurt | rijndael_enc | select | sha | spectral | startup | v32_benc | Geo. Mean
Relative ACET | 0.9051 | 0.9581 | 0.7077 | 1.074 | 0.9896 | 0.5213 | 0.7717 | 0.8893 | 0.9454 | 0.8918 | 1.1075 | 0.6329 | 0.6616 | 0.8108 | 0.9045 | 1.068 | 1.127 | 1.0166 | 1.1063 | 0.9287 | 0.6288 | 0.8793 | 0.8777 | 0.8524 | 0.8322 | 0.8288 | 0.8463 | 0.7585 | 0.579 | 0.7968 | 0.7956 | 0.7566 | 0.9868 | 0.5957 | 0.6889 | 0.8775 | 0.9329 | 0.6432 | 0.6949 | 1.0425 | 0.9002 | 1.0129 | 0.9814 | 0.963 | 0.885 | 0.9877 | 0.84761
100% = ACET using Standard Graph Coloring (highest degree)
-6% – -12%

## Slide 59: Discussion
WCETEST reductions from 6.9% up to 75.9%, on average 33.9%.
Allocation of all 46 benchmarks: total of 1,979 WCET analyses.
Run-time of WCET graph coloring: 12:15 hours for all 46 benchmarks  16 minutes per benchmark on average
ACET reductions of up to 47.9%, but decreases of up to 12.7%. On average, 15.2% ACET reduction.
Benchmarks behave very different w.r.t. WCETEST and ACET: gsm family: 51.5% – 66.2% WCETEST reduction 6.8% – 12.7% ACET degradation
Reason: WCET graph coloring avoids spilling along WCEP but inserts spill code at other places in the CFG which are frequently executed in an average-case scenario.

## Slide 60: Conclusions
Comparison with Consequences for WCETEST Optimizations
WCET-aware optimizations...
... mandatorily need detailed knowledge of the WCEP
WCET graph coloring considers the WCEP
... always have to be aware that the WCEP can change after each individual optimization decision
WCET graph coloring updates the WCEP after each modification of the code
... should take the decision where to optimize something not only based on local information, but should always consider the global effects of an optimization decision
WCET graph coloring is greedy heuristic that is driven solely by local data per basic block

## Slide 61: Chapter Contents
WCET-Aware Compilation
  Introduction
    Integration of a WCET Timing Model into a Compiler
    Challenges for WCET-Aware Optimization
  Procedure Cloning & Positioning
    WCET-Aware Procedure Cloning
    Procedure Positioning for Cache Miss Reduction
  Register Allocation
    Problem of Classical Graph Coloring
    WCET-Aware Graph Coloring
  Scratchpad Allocation of Data and Code
    Allocation of global Data
    Allocation of Basic Blocks

## Slide 62: In the Following: Harvard Architectures
Separate busses and memories for code and data
Scratchpad allocation of code and data can be solved independently from each other
Two separate ILPs for these optimizations
Non-Harvard architectures with unified busses and memories for code and data: Straightforward combination of both ILPs
Processor
D-SPM
Main Data Memory
P-SPM
Main Code Memory

## Slide 63: ILP for WCET-aware SPM Allocation of Data
Goal
Determine set of data objects (global variables or static local variables) to be allocated to the data SPM,
such that selected data objects lead to overall minimization of WCETEST
under consideration of switching WCEPs.
Approach
Integer-linear programming (ILP)
Optimality of results
Notation: Upper-case letters  constants, lower-case letters  variables

## Slide 64: Decision Variables & Costs
Binary decision variables per data object:
Costs of basic block bj: cj models the WCETEST of bj, depending on whether the data objects accessed by bj are allocated to main memory or SPM, resp. Cj: bj’s WCETEST if all data objects reside in main memory Gi,j: WCET reduction of bj if data object di is assigned to SPM

## Slide 65: Intraprocedural Control Flow (1)
Treat body of inner- most loop like acyclic sub-graph
Fold loop
Costs of :
Continue with next innermost loop
Modeling of a function’s control flow:
A
C
B
D
E
Acyclic sub-graphs:
(Reducible) Loops:
G
F
H
I
J
= WCET of longest path starting at A
Loop L
G, H, I
[V. Suhendra et al. WCET Centric Data Allocation to Scratchpad Memory. RTSS, Miami, 2005]

## Slide 66: Intraprocedural Control Flow (2)
Modeling of a function’s control flow:
  For sink nodes bj of an acyclic sub-graph, wj is set to the costs cj
  For all other nodes bj of an acyclic sub-graph, the WCET of the paths starting in bj must be greater or equal than the WCET of each successor bsucc, PLUS the costs cj of bj
  For each successor bsucc of bj, one constraint is created in the ILP
  Variable wj actually models all paths starting in bj. Due to the ≥ operator in the inequations, the maximum over all paths starting in wj is modeled
  Potential changes of the WCEP from one successor bsucc1 to another successor bsucc2 of bj are considered by construction

## Slide 67: Intraprocedural Control Flow (3)
Modeling of a function’s control flow:
  Reducible loops L have exactly one entry basic block bLentry
  By “ignoring” of the back-edge of a reducible loop L, the CFG of the loop body becomes acyclic
  Create constraints for acyclic loop body as shown on slide 65 (left part)
  Variable wLentry models WCETEST of the entire body of loop L if it is executed exactly once
  Multiplication of wLentry by the maximal number CLmax of iterations of L provides WCETEST for all executions of the loop
  Costs of L are equal to the WCETEST of L for all executions

## Slide 68: Interprocedural Control Flow
Modeling function calls:
  Each function has dedicated entry BB
  Variable models WCETEST of the longest path in that starts in
  models WCETEST of for exactly 1 execution of
  If calls function : Add to WCETEST of
Function calls in basic block :
  “Call penalty” for calling basic block:
  ILP constraint per basic block:

## Slide 69: Scratchpad Capacity and Objective Function
Scratchpad capacity constraint: The sum of the sizes of all data objects allocated onto the SPM is less than or equal to the totally available SPM capacity.
Objective function:
  models WCETEST of if is executed exactly once
  Variable models WCETEST of the entire program
  .
[F. Rotthowe. Scratchpad Allocation of Data for Worst-Case Execution Time Minimization (in German). Diploma Thesis, TU Dortmund, 2008]

## Slide 70: Rel. WCETEST after D-SPM Allocation of petrinet
Notable WCETEST reductions already for SPMs of only a few bytes
6 global variables of 72 bytes size in total
WCETEST reductions by 28.6% for 32 bytes SPM
X-Axis: Absolute SPM sizes
Y-Axis: 100% = WCETEST when not using SPM at all

## Slide 71: Rel. WCETEST after D-SPM Allocation of fsm
More steady WCETEST reductions for increasing SPM sizes
98 global variables à 4 bytes size each
WCETEST reductions by 21.4% for 256 bytes SPM
X-Axis: Absolute SPM sizes
Y-Axis: 100% = WCETEST when not using SPM at all

## Slide 72: Rel. WCETEST after D-SPM Allocation of 14 Benchmarks
Steady WCETEST reductions for increasing SPM sizes
WCETEST reductions from 2.7% – 20.6%
X-Axis: Absolute SPM sizes
Y-Axis: 100% = WCETEST when not using SPM at all
Chart: SPM Size [bytes]
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 40960
D-SPM | 0.97414 | 0.97029 | 0.95604 | 0.93468 | 0.91369 | 0.89991 | 0.87724 | 0.87711 | 0.86722 | 0.85134 | 0.82529 | 0.81063 | 0.80467 | 0.79841

## Slide 73: ILP for WCET-aware SPM Allocation of Code
Goal
Determine set of basic blocks to be allocated to the SPM
such that selected basic blocks lead to overall minimization of WCETEST
under consideration of switching WCEPs.
Approach
Integer-linear programming (ILP)
Optimality of results
Notation: Upper-case letters  constants, lower-case letters  variables

## Slide 74: Decision Variables & Costs
Binary decision variables per basic block:
Costs of basic block bi: models the WCETEST of if it is allocated to main memory or SPM, resp.
Modeling of the intraprocedural control flow: As before in the WCET-aware SPM allocation of data

## Slide 75: Cross-Memory Jumps
Allocation of consecutive basic blocks:
  Allocation of consecutive basic blocks in the CFG to different memories requires adaption/insertion of dedicated jumping code
  Cross-memory jumps are costly: Often need more than 1 instruction
  Jumping code: Variable overhead in terms of WCETEST and code size, depending on decision variables ( cf. chapter 7)
Jump Scenarios:
bi
bk
bj
bi
bk
bj
bi
bj
a) Implicit
b) Unconditional
c) Conditional

## Slide 76: Penalties for Cross-Memory Jumps
Jump Penalty (  Boolean XOR):
  Penalty for implicit jumps: High penalty if basic blocks i and j are placed in different memories
  Penalty for unconditional jumps:
    If bi and bj in different memories:
    If bi and bj adjacent in same memory: 0
    If bi and bj not adjacent in same memory:
  Conditional jumps: Obvious combination of and
bi
bk
bj
bj
bk
bj

## Slide 77: Jump Penalties and Interprocedural Control Flow
Jump penalties for basic block bi:
Penalty for function calls for basic block bi: If block calls function : Add WCETEST of to WCETEST of . Furthermore, add if function call is cross-memory call. If function call stays in the same memory, add only .

## Slide 78: Sizes of Basic Blocks
Constraint for all successors bsucc of bi:
Size of a basic block bi:
  Size of bi depends on actual jumping code for bi
  Size of jumping code of bi depends on jump scenario:
  Total size of basic block bi: Size Si of bi without any jumping code plus Size si of bi’s jumping code

## Slide 79: Scratchpad Capacity and Objective Function
Scratchpad capacity constraint: The sum of the sizes of all basic blocks allocated onto the SPM without jumping code, plus the size of jumping code in bi is less than or equal to the totally available SPM capacity.
Objective function:
[H. Falk, J. C. Kleinsorge. Optimal Static WCET-aware Scratchpad Allocation of Program Code. DAC, San Francisco, 2009]

## Slide 80: Determination of the Constants of the ILPs (1)
WCETEST of BB bi for SPM and main memory:
,
Max. iteration count of loop L:
Size of BB bi:
SPM size = 47 kB
SPM access = 1 cycle
Flash access = 6 cycles
Other parameters hard-coded:
, , …

## Slide 81: Determination of the Constants of the ILPs (2)
WCETEST , per basic block for both memories: Determined by two WCET analyses, one in which all basic blocks lie in the SPM, one with all blocks in main memory.
Max. iteration count of loops : Either annotated in the source code using flow facts, or determined by WCC’s automatic loop bound analysis.
Size of a basic block without jumping code: By simple enumeration of all LIR operations
Size of the scratchpad: Taken from WCC’s memory hierarchy specifications
Remaining parameters determined experimentally: = 16 = 8 = = 10 = 12

## Slide 82: Rel. WCETEST after P-SPM Allocation of g721_encode
Steady WCETEST decreases for increasing SPM sizes
WCETEST reductions from 29% – 48%
X-Axis: SPM size = x% of benchmark’s code size
Y-Axis: 100% = WCETEST when not using SPM at all

## Slide 83: Rel. WCETEST after P-SPM Allocation of cover
Stepwise WCETEST decreases: Useful content allocated to SPM only at 40%, 70% and 100% relative SPM size
WCETEST reductions of 10%, 35% and 44%
X-Axis: SPM size = x% of benchmark’s code size
Y-Axis: 100% = WCETEST when not using SPM at all

## Slide 84: Rel. WCETEST after P-SPM Allocation of md5
Almost invariable WCETEST reductions for all SPM sizes: 40% - 44%
ILP clearly finds tiny but time-critical hot-spot of md5 and allocates it to SPM
X-Axis: SPM size = x% of benchmark’s code size
Y-Axis: 100% = WCETEST when not using SPM at all

## Slide 85: Rel. WCETEST after P-SPM Allocation of 73 Benchmarks
Steady WCETEST reductions for increasing SPM sizes
WCETEST reductions from 8% – 41%
X-Axis: SPM size = x% of benchmark’s code size
Y-Axis: 100% = WCETEST when not using SPM at all
Chart: Relative SPM Size [%]
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
P-SPM Average | 0.91402 | 0.85229 | 0.81928 | 0.80307 | 0.77248 | 0.72736 | 0.71375 | 0.66547 | 0.64197 | 0.58607

## Slide 86: Conclusions
Comparison with Consequences for WCETEST Optimizations
WCET-aware optimizations...
... mandatorily need detailed knowledge of the WCEP
SPM allocations consider the WCEP
... always have to be aware that the WCEP can change after each individual optimization decision
SPM allocations inherently capture WCEP changes inside the ILP
... should take the decision where to optimize something not only based on local information, but should always consider the global effects of an optimization decision
Objective functions of the ILPs model the global WCET of a program that is subject to minimization.

## Slide 87: References
WCC Compiler Infrastructure
H. Falk, P. Lokuciejewski. A compiler framework for the reduction of worst-case execution times. Springer Real-Time Systems 46(2), October 2010.

## Slide 88: Summary
Compilers for WCETEST Minimization
Integration of a formal WCET timing model into compiler
Challenge: To consider unstable WCEPs in the course of optimizations
WCET-aware Optimizations
Procedure Cloning & Positioning: Greedy heuristics that determine current WCEP via repeated WCET analyses
Register allocation: cyclic dependencies between register allocation and WCET analysis; graph coloring along the always current WCEP
Scratchpad allocations: Inherent modelling of WCEP in the ILPs; eliminates need for repeated WCET analyses during optimization